Neuron Modeling w/ Prof. Rattay

# 1. Functional Electrical Nerve Stimulation (FES)
Applications of FES:
- Cardiac pacemakers [1952]
- Phrenic (diaphragm) pacemakers (respiratory insufficiency)
- Paralyzed muscles
- Incontinence (bladder control, bowel incontinence)
- Spasm improvements
- Blindness (Retinal implants)
- Deafness (Cochlea implants)

1952: Hodgkin and Huxley discover excitability of nerve fibers along a giant squid axon.
Auditory goes back to Volta in 1790. 1957 Djourno and Eyries found that they could stimulate the auditory nerve of a deaf patient.

APs (Action Potentials) propagate along axons (nerve fibers) to transmit information. The AP has a certain strength and has to be high enough to excite other cells.

Figure 1: Electric model of a membrane. On both sides different ionic concentrations are apparent. This is shown as the battery (voltage source) in the model.
For the model a voltage source, capacitor and a nonlinear resistance are needed.
Vi … Inside potential
Ve … External potential
V = Vi – Vb
Current through the membrane as diff. equation:
Im = Icapacity + Iionic = C * dV/dt + V/R
C … membrane capacity
R … non-linear resistance, function of voltage V and time t.

Figure 2: The propagation of a signal along an axon can be modeled as a ladder network.

# 2. Design of the Nervous System
Most neurons of the body are contained in the central nervous system.
Peripheral neurons are referred to as peripheral neurons and motor neurons.

A neuron consists of a soma (cell body) and 1+ processes/extensions. Theses processes are known as dendrites and the axon. The axon is a the longest dendrite. The axon forks into many fibers in its end, which is called the synapse. The synapses are in very close contact to other cells and allow for the propagation of stimuli via the synaptic cleft.
Neural activity at the soma can cause small changes in voltage which may propagate to the axon, when a threshold is passed. The impulse will be sent along the axon. (All-or-nothing Law)

Nerve fibers consist of a long cylinder of axoplasm surrounded by electrically excitable membranes. Conducting velocity depends on thickness and insulation. Unmyelinated fibers can be found mostly in the CNS and in small vertebrates.
Speed of unmyelinated fibers: v = 1.1 * sqrt(diameter)

Larger fibers are usually myelinated. Myelin is made by Schwann cells, wrapping around the fibers tightly. More and more Schwann cells wrap around and squeeze out the Schwann cell’s cytoplasm, leading to a very thick cell membrane for the axon.
Myelinated fibers have a conduction velocity in m/s of 4.5 * diameter (µm), when diameter is <11µm, and 6 * diameter (µm) when >11µm. For 10: 45m/s
At the Node of Ranvier a high concentration of ion channels is found. The Node of Ranvier can be seen in measurements as small saw-like spikes in the AP.

There are ~80% excitatory pyramidal neurons and ~20% inhibitory interneurons in the brain.
# 3. The Excitability of Cells
1868: Bernstein’s hypothesis
Living cells are composed of electrolytic interiors surrounded by a membrane impermeable to ions.
Different ionic concentrations on both sides lead to a electrical potential or voltage.
At rest, the inside potential is around 70mV smaller than the outside, referred to as polarized state.
When they become activated (depolarized state) they change from -70mV to 50mV. Then a repolarization happens with a negative overshoot (hyperpolarization).

Nernst equation:

 R*T/F ~ 25mV
 z … valence (for Na+ ions, z = 1)

The Nernst equation in the biological context is a measurement of the tendency of ions to cross a cell membrane. In general it is a electrochemistral equation relating the reduction potential of a (redox-)reaction to electrode potential, temperature.
It can be used to describe the equilibrium voltage at which no ions travel through the membrane/channels.

Goldman equation:

PK … permeability in cm/sec
K,Na,Cl … concentrations on inside and outside

The Goldman equation can be used to calculate the membrane potential w/ multiple ion channels.
It can be seen as a generalization of the Nernst equation.
The sum of all ionic currents is zero in the Goldman equation, and therefore the channels do not have to be in equilibrium, but the overall activity is.
It was developed before channels were discovered, so permeability is used.

Membranes have ion channels. When these channels open ions flow through them and change the inside/outside concentrations. Channels work either voltage gated, mechanically gated or chemically gated.
Chemically gated channels in synapses may change the local membrane potential, leading to the activation of voltage gated channels. These are unidirectional. There are also synaptic clefts with voltage gated channels, which are bidirectional. PSPs (Post Synaptic Potentials) may not be high enough to cause an action potential, however if enough pulses come in a short time the PSPs may sum up to cause the membrane to become depolarized leading to an AP. There are excitatory and inhibitory PSPs contributing to this. There are also excitatory synapses (depolarization→ AP), and inhibitory synapses (hyperpolarization).
Ions are returned into the cell (or out of) with pumps.

Figure 3: Conduction of an AP along an axon
## Izikhevich models
Often bursting is used to cause an AP. Bursting is a state in which a neuron repeatedly fires discrete groups of bursts or spikes.

Model:
v’ = 0.05v² + 5v + 140 – u + I
u’ = a(bv – u)
Auxiliary after-spike resetting when v >= 30mV:
v ← c
u ← u + d
v … represents membrane potential
u … represents membrane recovery (activation of K channels, deactivation of Na channels)

Model is well suited for computational simulation, as the neuronal behaviours in the figure below can be mimicked and it is only two differential equations.
Figure 4: Excitatory: RS, IB, CH; Inhibitory: FS, LTS; Cortex-Neurons: TC
# 4. Space Clamp Experiment of Hodgkin Huxley – Non-propagating Action Potentials
H&H assumed that a gating mechanism must be responsible for the ionic transport along the axon of sodium and potassium.

They inserted a stimulating electrode along the axis of the axon. A second electrode was inserted in the membrane to measure voltage between inside and outside.
In the experiment no current flow along the axis is apparent and all parts of the membrane work under the same conditions, because of isopotentials on the inside and outside. This is the local model.

In the voltage clamp experiment the voltage is constant, which allows to measure the ionic currents for controlled voltage steps. Certain ionic currents can be determined by influencing channel activity with certain blocker molecules or using different outside fluids.
The injected current can be measured to find the conductance of the ionic currents.

Figure 5: Voltage has to follow the current in the second figure. First a quick influx of Na+ with slow outward flux of K+.

Injected current Iinj has to pass the membrane as capacitive or ionic current.
Iinj = Iionic + C * dV/dt
Iinj = INa + IK

Potassium was measured by using bigger cations on the outside which couldn’t pass the channels, so only potassium passed through.
By the formula above INa was then measured.

INa ~ gNa (and vice versa for K)
g … conductance

The Hodgkin-Huxley (HH) model consists of four differential equations:

gL … leakage conductance
m … sodium channel open activation gates probability
h … sodium channel open inactivate gates probability
n … potassium channel open probability
k … thermic coefficient
ist … injected current divided by membrane area involved

Time course for m, h, n are seen in HH-2, 3, 4 above, found by using experimental data of H&H.

V = Vi – Ve – Vrest
V = 0mV
Vrest = -70mV

Calculations depend on diamter and size of measured area. Therefore we use 1cm² of area. Currents become current densities and c the capacity per cm².

As Iinj = Iionic + C * dV/dt it follows:
dV/dt = ( - Iionic + Ist)/c → HH model as seen above.

The reaction speeds up with higher k. Potassium channel conductance increases monotonically, while sodium channel conductance rises fast and falls just as fast. H&H assumed that there must be an inactivation gate.

Rheobase: Minimal current needed to excite a nerve. (due to current leakage)
Chronaxie: Time of an AP when ist = 2*iRheobase

# 5. Comparment Models

Figure 6: Multicompartment Model (Rattay 2003)
This is a non-typical cell. Dendrite is myelinated (peripheral axon).In cochlea cells the soma would normally be myelinated as well. The soma takes a lot of current and time.
At the terminal node a much higher density of ion-channel can be found.

A neuron can be represented an electric network as seen in the figures above. A current injected at a compartment has to cross the membrane as ionic or capacitive current and has to go to the right and left, as Kirchhoff’s law says that sum(I) = 0.
Compartment models can be used to simulate spiking using FEM.
Neuron behavior strongly differs depending on size, shape and other characteristics.

Internodes (myelinated areas) let some ions through as well and should not be neglected.

## Activating function
In compartment models the activating function can be used to estimate whether an electrical field may cause an action potential on an axon or a neuron. It points out locations of high hyperpolarization and depolarization caused by the electrical field acting upon the nerve fiber. Positive values of f suggest a depolarization of the membrane potential and negative values a hyperpolarization of the membrane potential.

fn is in V/sec. fn represents the rate of membrane voltage change in every compartment activated by the extracellular field, if the neuron is currently in the resting state.

A new activating function has been introduced by McNeal in which membrane conductance and capacity are assumed to be 0, which simplifies f substantially. The function becomes proportional to the second difference of the extracellular potential along fibers.

Noise current is proportional to the square root of the number of sodium channels.
# Retina Stimulation
Patients may lose vision due to problems with their retina. In many cases they still have functioning nerve cells (ganglion cells, bipolar cells) relaying input to the brain.
A compartment model for extracellular excitation of RGCs (Retinal ganglion cells) has been developed to find out where RGCs are most excitable.
Compartment models have been used to model the RGC of an amphibian mudpuppy.
Axons of RGCs have unmyelinated axons.
Two models have been created.
Several types of neurons in the retina may never cause an action potential, but may heavily contribute to them by releasing neurotransmitters.

-----------
Other
Calcium currents often have significant influence on spiking patterns.
FitzHugh model: Prototype of an excitatory system e.g. neuron or axon. If the external current surpasses a threshold the system performs a characteristic excursio in the (v,w)-phase space, before v = v0 and w = w0 again. v … Membrane potential, w … recovery.
(v0, w0) → stationary point in the system
v’ = v – 1/3 v³ – w + Iext
tau * w’ = v – a – bw
Figure 7: vw phase space

# 5. Modeling the Membrane
# 6. Spike Propagation
# 7. Extracellular Stimulation of Fibers